## Slide 1
DESIGN AND SIMULATION OF A 4-BIT DIGITAL CODE LOCK SYSTEM
Using Combinational and Sequential Logic
TEAM MEMBERS
1. 2620090125 — K. CHARAN KUMAR REDDY 2. 2620090134 — E. SHARAN TEJA 3. 2620090136 — Y. TARUN KUMAR
Department of Electronics / DDCA • Academic Year 2026–27

## Slide 2
2. Introduction
Digital security using logic circuits
• Digital code locks provide access only when a correct input sequence or code is entered.
• A 4-bit code lock uses four binary inputs, giving 16 possible combinations from 0000 to 1111.
• Combinational logic determines whether the entered code matches the preset code.
• Sequential logic adds memory, so the system can track steps, lock state, or a valid entry sequence.
• The project demonstrates the design and simulation of a simple, low-cost digital security system.
DDCA Project • 4-Bit Digital Code Lock | 2/12

## Slide 3
3. Problem Statement
Why a digital code-lock system is needed
Problem
Basic access systems may rely on keys
or simple switches that can be lost, copied,
or operated without sequence control.
Limitations
A purely combinational circuit has no
memory of previous inputs, making it
unsuitable for sequence-dependent
access control.
Need
A compact system should verify a 4-bit code,
remember the required state, and provide
clear LOCK/UNLOCK outputs.
• Design a system that combines immediate logic comparison with state/memory elements.
• Verify the design through simulation before hardware implementation.
DDCA Project • 4-Bit Digital Code Lock | 3/12

## Slide 4
4. Objectives
Specific goals of the project
01 Design
Develop a 4-bit digital code-lock circuit using
logic gates and memory elements.
02 Compare
Compare the entered 4-bit code with a
predefined valid code.
03 Sequence
Use sequential logic to retain system state and
support controlled unlocking.
04 Indicate
Generate clear LOCK and UNLOCK
status outputs.
05 Simulate
Test correct and incorrect code conditions
using simulation.
06 Evaluate
Discuss reliability, limitations, and possible
improvements.
DDCA Project • 4-Bit Digital Code Lock | 4/12

## Slide 5
5. Literature Survey / Existing System
Common approaches to digital access control
Mechanical Lock
• Physical key is required • Simple and familiar • Key can be lost or duplicated • No digital state tracking
Keypad / Digital Lock
• User enters a code • Electronic comparison is possible • Can use LEDs, buzzers or displays • More flexible than a key
Proposed Learning Model
• 4-bit binary code • Combinational code comparison • Sequential state/memory • Easy to simulate and understand
DDCA Project • 4-Bit Digital Code Lock | 5/12

## Slide 6
6. Proposed System
A hybrid combinational + sequential digital lock
• Four input switches represent the entered binary code.
• XNOR logic compares each input bit with the corresponding preset code bit.
• AND logic combines the four equality signals to produce a VALID-CODE signal.
• A flip-flop or state register stores the lock/unlock state and prevents the output from depending only on an instantaneous input.
• Reset returns the system to the LOCKED state; a correct code can move the system to UNLOCKED.
• LEDs or logic probes display the current status during simulation.
DDCA Project • 4-Bit Digital Code Lock | 6/12

## Slide 7
7. System Architecture / Block Diagram
Signal flow from code entry to access decision
4-BIT INPUT SWITCHES
CODE COMPARATOR
VALID CODE LOGIC
SEQUENTIAL STATE
LOCK / UNLOCK OUTPUT
RESET → LOCKED STATE
• Data path: Inputs → bit comparison → code validity → state update → output.
• The sequential block provides memory for the system state.
DDCA Project • 4-Bit Digital Code Lock | 7/12

## Slide 8
8. Methodology / Implementation
Design steps and circuit components
1. Define 4-bit code
Select a preset code and input representation.
2. Build comparator
Use four XNOR gates to test bit-by-bit equality.
3. Combine results
Use AND logic to create the VALID-CODE signal.
4. Add memory
Use a flip-flop/state element for
LOCKED/UNLOCKED status.
5. Connect outputs
Drive LOCK/UNLOCK LEDs or logic probes.
6. Simulate & test
Apply correct and incorrect combinations
and observe outputs.
DDCA Project • 4-Bit Digital Code Lock | 8/12

## Slide 9
9. Logic Design & Truth Table
Example preset code: 1011
A B C D
VALID
UNLOCK*
1011
1
1
0000
0
0
1111
0
0
1001
0
0
0011
0
0
DDCA Project • 4-Bit Digital Code Lock | 9/12

## Slide 10
10. Simulation & Results
Expected behavior of the digital lock
Simulation test cases
1011
1
UNLOCKED
Correct code
1010
0
LOCKED
One-bit error
0011
0
LOCKED
Incorrect code
1111
0
LOCKED
Incorrect code
RESET
—
LOCKED
Reset condition
Result: only the predefined 4-bit code produces a valid access request; reset restores the locked state.
DDCA Project • 4-Bit Digital Code Lock | 10/12

## Slide 11
11. Results and Discussion
Performance, advantages and limitations
Observed / Expected Results
✓ Correct code detected ✓ Wrong codes rejected ✓ Sequential state retains LOCK/UNLOCK ✓ Reset returns to LOCKED ✓ Logic is easy to verify in simulation
Advantages
• Low component complexity • Fast logic response • Easy to simulate • Demonstrates combinational + sequential
concepts • Can be extended with a keypad or display
Limitations
• 4-bit code offers only 16 combinations • No user authentication beyond the code • Basic design has no alarm/lockout timer • Hardware implementation needs
debouncing and protection
DDCA Project • 4-Bit Digital Code Lock | 11/12

## Slide 12
Thank You
K. Charan Kumar Reddy • E. Sharan Teja • Y. Tarun Kumar